## Slide 1
Covert Channels:
Hiding Data In Plain Sight
Capt Daniel Fitzgerald
22 JUL 2025

## Slide 2
Categorize based on patterns
A Pattern-based Survey and Categorization of Network Covert Channel Techniques by Steffen Wendzel, Sebastian Zander, Bernhard Fechner, Christian Herdin [Wendzel 2014]
Whitepaper: https://arxiv.org/pdf/1406.2901.pdf
Author’s website: https://www.wendzel.de/
Current: https://ih-patterns.blogspot.com/p/test.html
History of updates: https://wendzel.de/dr.org/files/Papers/EICC22_poster.pdf
Author’s addresses: S. Wendzel, Fraunhofer Institute for Communication, Information Processing and Ergonomics FKIE, Bonn, Germany; S. Zander, Centre for Advanced Internet Architectures, Swinburne University of Technology, Melbourne, Australia; B. Fechner, University of Augsburg, Department of Systems and Networking, Augsburg, Germany; C. Herdin, University of Rostock, Department of Computer Science, Rostock, Germany Permission to make digital or hard copies of part or all of this work for personal or classroom use is granted without fee provided that copies are not made or distributed for profit or commercial advantage and that copies show this notice on the first page or initial screen of a display along with the full citation. Copyrights for components of this work owned by others than ACM must be honored. Abstracting with credit is permitted. To copy otherwise, to republish, to post on servers, to redistribute to lists, or to use any component of this work in other works requires prior specific permission and/or a fee. Permissions may be requested from Publications Dept., ACM, Inc., 2 Penn Plaza, Suite 701, New York, NY 10121-0701 USA, fax +1 (212) 869-0481, or permissions@acm.org. c 2014 ACM 0360-0300/2014/-ART1 $15.00 DOI:http://dx.doi.org/10.1145/0000000.0000000
Evaluating Covert Channels
Notes: https://www.wendzel.de/
https://ih-patterns.blogspot.com/p/test.html
[1] S. Wendzel, S. Zander, B. Fechner, C. Herdin: Pattern-based Survey and Categorization of Network Covert Channel Techniques, ACM Computing Surveys, Vol. 47, Issue 3, pp. 50:1-26, ACM, 2015. An early version of the article is available here: download. [2] W. Mazurczyk, S. Wendzel, S. Zander, A. Houmansadr, K. Szczypiorski: Information Hiding in Communication Networks, Wiley, 2016. Chapters 3 and 8 contain discussions on hiding patterns, basically on the basis of [1] but with an extension of timing-based patterns. [3] W. Mazurczyk, S. Wendzel, K. Cabaj: Towards Deriving Insights into Data Hiding Methods Using Pattern-based Approach, in Proc. Second International Workshop on Criminal Use of Information Hiding (CUING 2018) at ARES, pp. 10:1-10:10, ACM, 2018.
[4] A. Velinov, A. Mileva, S. Wendzel, W. Mazurczyk: Covert Channels in MQTT-based Internet of Things, IEEE ACCESS, Vol. 7, pp. 161899-161915, 2019.
[5] A. Mileva, A. Velinov, L. Hartmann, S. Wendzel, W. Mazurczyk: Comprehensive Analysis of MQTT 5.0 Susceptibility to Network Covert Channels, Computers & Security, Elsevier, 2021.
[6] L. Hartmann, S. Zillien, S. Wendzel: Reset- and Reconnection-based Covert Channels in CoAP. In: Proc. European Interdisciplinary Cybersecurity Conference (EICC), 2021.

## Slide 3
Video Introduction to Patterns: https://www.youtube.com/watch?v=0ztPHur0LUY
Evaluating Covert Channels
Notes: https://www.wendzel.de/
https://ih-patterns.blogspot.com/p/test.html
[1] S. Wendzel, S. Zander, B. Fechner, C. Herdin: Pattern-based Survey and Categorization of Network Covert Channel Techniques, ACM Computing Surveys, Vol. 47, Issue 3, pp. 50:1-26, ACM, 2015. An early version of the article is available here: download. [2] W. Mazurczyk, S. Wendzel, S. Zander, A. Houmansadr, K. Szczypiorski: Information Hiding in Communication Networks, Wiley, 2016. Chapters 3 and 8 contain discussions on hiding patterns, basically on the basis of [1] but with an extension of timing-based patterns. [3] W. Mazurczyk, S. Wendzel, K. Cabaj: Towards Deriving Insights into Data Hiding Methods Using Pattern-based Approach, in Proc. Second International Workshop on Criminal Use of Information Hiding (CUING 2018) at ARES, pp. 10:1-10:10, ACM, 2018.
[4] A. Velinov, A. Mileva, S. Wendzel, W. Mazurczyk: Covert Channels in MQTT-based Internet of Things, IEEE ACCESS, Vol. 7, pp. 161899-161915, 2019.
[5] A. Mileva, A. Velinov, L. Hartmann, S. Wendzel, W. Mazurczyk: Comprehensive Analysis of MQTT 5.0 Susceptibility to Network Covert Channels, Computers & Security, Elsevier, 2021.
[6] L. Hartmann, S. Zillien, S. Wendzel: Reset- and Reconnection-based Covert Channels in CoAP. In: Proc. European Interdisciplinary Cybersecurity Conference (EICC), 2021.

## Slide 4
Evaluating Covert Channels
Original as of 2015
[Wendzel 2015]
Notes: [1] S. Wendzel, S. Zander, B. Fechner, C. Herdin: Pattern-based Survey and Categorization of Network Covert Channel Techniques, ACM Computing Surveys, Vol. 47, Issue 3, pp. 50:1-26, ACM, 2015. An early version of the article is available here: download.

## Slide 5
Updated as of 25 Mar 2022
[https://ih-patterns.blogspot.com/p/test.html]
Notes: [1] S. Wendzel, S. Zander, B. Fechner, C. Herdin: Pattern-based Survey and Categorization of Network Covert Channel Techniques, ACM Computing Surveys, Vol. 47, Issue 3, pp. 50:1-26, ACM, 2015. An early version of the article is available here: download. [2] W. Mazurczyk, S. Wendzel, S. Zander, A. Houmansadr, K. Szczypiorski: Information Hiding in Communication Networks, Wiley, 2016. Chapters 3 and 8 contain discussions on hiding patterns, basically on the basis of [1] but with an extension of timing-based patterns. [3] W. Mazurczyk, S. Wendzel, K. Cabaj: Towards Deriving Insights into Data Hiding Methods Using Pattern-based Approach, in Proc. Second International Workshop on Criminal Use of Information Hiding (CUING 2018) at ARES, pp. 10:1-10:10, ACM, 2018.
[4] A. Velinov, A. Mileva, S. Wendzel, W. Mazurczyk: Covert Channels in MQTT-based Internet of Things, IEEE ACCESS, Vol. 7, pp. 161899-161915, 2019.
[5] A. Mileva, A. Velinov, L. Hartmann, S. Wendzel, W. Mazurczyk: Comprehensive Analysis of MQTT 5.0 Susceptibility to Network Covert Channels, Computers & Security, Elsevier, 2021.
[6] L. Hartmann, S. Zillien, S. Wendzel: Reset- and Reconnection-based Covert Channels in CoAP. In: Proc. European Interdisciplinary Cybersecurity Conference (EICC), 2021.

## Slide 6
Evaluating Covert Channels
109 covert channels analyzed fit into 11 different patterns
69.7% can be categorized into only 4 different patterns
[Wendzel 2014]
Notes: Screenshot from A Pattern-based Survey and Categorization of Network Covert Channel Techniques by Steffen Wendzel
https://arxiv.org/pdf/1406.2901.pdf
[1] S. Wendzel, S. Zander, B. Fechner, C. Herdin: Pattern-based Survey and Categorization of Network Covert Channel Techniques, ACM Computing Surveys, Vol. 47, Issue 3, pp. 50:1-26, ACM, 2015. An early version of the article is available here: download.

## Slide 7
PS1. Size Modulation Pattern
  Illustration: Uses size of a header element or PDU to encode message
  Context: Storage -> Modification of Non-Payload -> Structure Modifying
  Evidence:
    Data block length in LAN frames
    Padding field’s size in 802.3 frames
    Message length of network packets
    Size of IPSec messages
    IP fragment sizes
Evaluating Covert Channels

## Slide 8
PS2. Sequence Pattern
  Illustration: Alters the sequence of header/PDU elements to encode message
  Context: Storage -> Modification of Non-Payload -> Structure Modifying
  Evidence:
    Sequence of HTTP header fields
    Sequence of DHCP options
    Sequence of FTP commands
Evaluating Covert Channels

## Slide 9
PS2.a. Position Pattern
  Illustration: Alters position of a given header/PDU element
  Context: Storage -> Non-Payload -> Structure Modifying -> Sequence
  Evidence:
    Position of IPv4 option in options list
    Position of IPv6 extension header in extension header list
PS2.b. Number of Elements Pattern
  Illustration: The number of header/PDU elements transferred
  Context: Storage -> Non-Payload -> Structure Modifying -> Sequence
  Evidence:
    Number of options placed in an IPv4 packet
    Modulate number of fragments created from an original IP packet
    Modulate number of options placed in a DHCP packet
Evaluating Covert Channels

## Slide 10
PS3. Add Redundancy Pattern*
  Illustration: Creates new space within a given header element/PDU
  Context: Storage -> Non-Payload -> Structure Modifying
  Evidence:
    Generate packets with IPv4 options
    Create new IPv6 destination option
    Extend HTTP headers with additional fields
    Manipulate pointer and length values for IPv4 record route option
    Add random bytes to an encrypted SSH message
    Extend SMTP packet headers with additional fields
    Hide data in unused bits of the DHCP chaddr field
    Encapsulate IP packet with smaller size than specified in Ethernet frame
Evaluating Covert Channels

## Slide 11
PS10. Random Value Pattern*
  Illustration: Embed data in header element containing “random” value
  Context: Storage -> Non-Payload -> Structure Preserving -> Modification of an Attribute
  Evidence:
    IPv4 Identifier field
    First sequence number of a TCP connection (ISN)
    TCP ISN using a bounce server
    DHCP xid field
    SSH MAC field
Evaluating Covert Channels

## Slide 12
PS11. Value Modulation Pattern*
  Illustration: Channel selects one of n values a header element can contain
  Context: Storage -> Non-Payload -> Structure Preserving -> Modification of an Attribute
  Evidence:
    Send frame to one of n available addresses in local network
    Encode info by n of the possible IP header TTL values
    Encode info by n of possible Hop Limit values in IPv6 header
    Encode info by sending packet using one of n possible application layer protocols
    Encode info in the target IP of ARP messages
    Send IPSec packets from one VPN site to specific destination IPs within another VPN site
Evaluating Covert Channels

## Slide 13
PS11.a. Case Pattern
  Illustration: Case-modification of letters in header elements
  Context: Storage->Non-Payload->Structure Preserving->Modification of Attribute-> Value Modulation
  Evidence:
    Case modification in HTTP headers or SMTP/POP3/etc. commands and headers
PS11.b. Least Significant Bit (LSB) Pattern
  Illustration: Uses LSB of header elements
  Context: Storage->Non-Payload->Structure Preserving->Modification of Attribute-> Value Modulation
  Evidence:
    IPv4 timestamp option by sending at even/odd times
    Use LSB of IPv4 TTL or IPv6 Hop Limit or Hop Count field of BACnet protocol
Evaluating Covert Channels

## Slide 14
PS11.c. Value Influencing Pattern
  Illustration: Sender (directly or indirectly) influences some (out of n possible) values in a way that a covert channel receiver can determine the value
  Context: Storage->Non-Payload->Structure Preserving->Modification of Attribute-> Value Modulation
  Evidence:
    A. Velinov, A. Mileva, S. Wendzel, W. Mazurczyk: Covert Channels in MQTT-based Internet of Things, IEEE ACCESS, Vol. 7, pp. 161899-161915, 2019
Evaluating Covert Channels

## Slide 15
PS12. Reserved/Unused Pattern*
  Illustration: Encode data into reserved or unused header/PDU element
  Context: Storage->Non-Payload->Structure Preserving->Modification of an Attribute
  Evidence:
    Unused fields in IPv4, e.g. ID field, DF flag, Reserved flag
    Unused fields in IPv6 header or extension headers
    ICMP echo payload
    Unused fields in BACnet header
    Place data behind string termination symbol of sname/file DHCP fields
    DS field of outbound IPSec connections
    ECN field in IPSec connections
Evaluating Covert Channels

## Slide 16
PS20. Payload Field Size Modulation
  Illustration: Uses a size of the payload field of a flow's PDUs/messages to encode the hidden message. Variant of Size Modulation.
  Context: Storage->Payload->User-data Agnostic
  Evidence:
    Modulate size of data block field in Ethernet frames
    Any other method that modulates size of payload field in any network protocol
Evaluating Covert Channels

## Slide 17
PS21. User-data Corruption
  Illustration: Related to the cases when steganographic methods do not take into account what kind of user-data is carried within a payload field and/or what its characteristic is (blind modification). It can be applied to single PDUs or to multiple PDUs (a flow). This typically happens if parts of (or the whole) user-data is replaced with secret bits and thus the user-data is corrupted/lost.
  Context: Storage->Payload->User-data Agnostic
  Evidence:
    W. Mazurczyk, S. Wendzel, K. Cabaj: Towards Deriving Insights into Data Hiding Methods Using Pattern-based Approach, in Proc. Second International Workshop on Criminal Use of Information Hiding (CUING 2018) at ARES, pp. 10:1-10:10, ACM, 2018.
Evaluating Covert Channels

## Slide 18
PS30. Modify Redundancy
  Illustration: Used when it is possible to exploit the redundancy of the user-data by means of transforming them in such a way that a free space for secret data is obtained. Similar to Add Redundancy but can also decrease redundancy and is applied to payload instead of meta-data.
  Context: Storage->Payload->User-data Aware
  Evidence:
    Compress existing user-data in order to make a space for secret data.
    Transform the VAD-enabled IP telephony voice stream into non-VAD one and fill the gaps using artificially generated RTP packets containing secret data.
    Approximate the F0 parameter of the Speex codec which carries information about the pitch of the speech signal and use the ``saved'' space for secret data.
Evaluating Covert Channels

## Slide 19
PS31. User-data Value Modulation and Reserved/Unused
  Illustration: Characteristic features of user-data can be utilized to store secret information. This includes applying methods like LSB modification to speech samples or digital images carried within the payload field. Compared with previous patterns this is a targeted modification. This pattern is analogous to the combination of the patterns.
  Context: Storage->Payload->User-data Aware
  Evidence:
    Encode a stream of information by spreading the encoded data across as much of the frequency spectrum as feasible (e.g. DSSS).
    Embeds secret data into a carrier audio signal by introducing an echo (a.k.a. echo hiding).
    Replacing the least significant bit of e.g. each voice sample with secret data (LSB).
Evaluating Covert Channels

## Slide 20
PT1. Inter-packet Times
  Illustration: Alters timing intervals between network PDUs (inter-arrival times)
  Context: Timing Channels->Protocol-agnostic
  Evidence:
    Timings between LAN frames sent
    Response time of HTTP server
    Timings between BACnet/IP packets
    Introduce artificial delays into inter-arrival times of SSH packets
    Record legitimate traffic sequence, partition sequence and replay the inter-arrival times of a particular partition
Evaluating Covert Channels

## Slide 21
PT2. Message Sequence Timing
  Illustration: Hidden data is encoded in the timing of message sequences, e.g. acknowledging every n'th received packet or sending commands m times.
  Context: Timing Channels->Protocol-agnostic
  Evidence:
    W. Mazurczyk, S. Wendzel, S. Zander, A. Houmansadr, K. Szczypiorski: Information Hiding in Communication Networks, Wiley, 2016. Chapters 3 and 8 contain discussions on hiding patterns, basically on the basis of [1] but with an extension of timing-based patterns.
Evaluating Covert Channels

## Slide 22
PT3. Rate/Throughput Pattern
  Illustration: Sender alters data rate of traffic flow from self or 3rd party
  Context: Timing Channels->Protocol-agnostic
  Evidence:
    Exhaust performance of a switch to affect the throughput of 3rd party connection
    Manipulate serial communication port’s throughput by delaying Clear to Send/Read to Send commands
    Directly alter data rate of legitimate channel
Evaluating Covert Channels

## Slide 23
PT10. Artificial Message/Packet Loss Pattern
  Illustration: Hidden information via artificial loss of transmitted messages (PDUs)
  Context: Timing Channels->Protocol-aware
  Evidence:
    W. Mazurczyk, S. Wendzel, S. Zander, A. Houmansadr, K. Szczypiorski: Information Hiding in Communication Networks, Wiley, 2016. Chapters 3 and 8 contain discussions on hiding patterns, basically on the basis of [1] but with an extension of timing-based patterns.
Evaluating Covert Channels

## Slide 24
PT11. Message Ordering Pattern
  Illustration: Encode data using synthetic PDU order for given number of PDUs flowing between sender and receiver
  Context: Timing Channels->Protocol-aware
  Evidence:
    Modify order of IPSec Authentication Header (AH) packets
    Modify order of IPSec ESP packets
    Modify order of TCP packets
    Modify order of IPSec packets for inbound/outbound VPN traffic
    Sender transfers frames in a way they are send before or after a legitimate user’s frames in CSMA/CD networks
Evaluating Covert Channels

## Slide 25
PT12. Re-Transmission Pattern
  Illustration: Channel re-transmits previously send/received PDUs
  Context: Timing Channels->Protocol-aware
  Evidence:
    Transfer selected DNS requests once/twice to encode bit per request
    Duplicate 802.11 packets
    Re-transmit selected TCP segments
    Do not ACK received packets in order to force sender to re-transmit
Evaluating Covert Channels

## Slide 26
PT13. Frame Collision Pattern
  Illustration: Sender causes artificial frame collisions to signal hidden information.
  Context: Timing Channels->Protocol-aware
  Evidence:
    W. Mazurczyk, S. Wendzel, S. Zander, A. Houmansadr, K. Szczypiorski: Information Hiding in Communication Networks, Wiley, 2016. Chapters 3 and 8 contain discussions on hiding patterns, basically on the basis of [1] but with an extension of timing-based patterns.
Evaluating Covert Channels
Notes:     Generate corrupted messages in broadcast erasure channels
    Transfer corrupted frames in 802.11
    MitM adversary between 2 VPN sites drops selected packets exchanged

## Slide 27
PT14. Temperature Pattern
  Illustration: Sender influences a third-party node's CPU temperature, e.g.\ using burst traffic. This influences the node's clock skew. The clock skew can then be interpreted by the covert receiver by interacting with the node.
  Context: Timing Channels->Protocol-aware
  Evidence:
    W. Mazurczyk, S. Wendzel, S. Zander, A. Houmansadr, K. Szczypiorski: Information Hiding in Communication Networks, Wiley, 2016. Chapters 3 and 8 contain discussions on hiding patterns, basically on the basis of [1] but with an extension of timing-based patterns.
Evaluating Covert Channels

## Slide 28
PT15. Artificial Reconnections
  Illustration: Employs artificial (forced) reconnections to transfer secret messages. The covert sender influences connection states of third-party nodes in a way that their connections to either a central element or a peer are terminated and then established again (i.e., a reconnect is performed).
  Context: Timing Channels->Protocol-aware
  Evidence:
    Aleksandra Mileva, Aleksandar Velinov, Laura Hartmann, Steffen Wendzel, Wojciech Mazurczyk: Comprehensive Analysis of MQTT 5.0 Susceptibility to Network Covert Channels, Computers & Security, Elsevier, 2021.
    Sebastian Zillien, Steffen Wendzel: Reconnection-based Covert Channels in Wireless Networks. In: Proc. 36th IFIP TC-11 International Information Security and Privacy Conference (IFIP SEC 2021). Springer, 2021.
Evaluating Covert Channels

## Slide 29
PT16. Artificial Resets
  Illustration: Covert sender causes a connection reset of third-party nodes, whose connection states are observed by one or more covert recievers.
  Context: Timing Channels->Protocol-aware
  Evidence:
    Laura Hartmann, Sebastian Zillien, Steffen Wendzel: Reset- and Reconnection-based Covert Channels in CoAP. In: Proc. European Interdisciplinary Cybersecurity Conference (EICC 2021). ACM, DOI: 10.1145/3487405.3487660
Evaluating Covert Channels
Notes: https://github.com/NIoSaT/CoAP-Covert-Channels features the first known implementation and is based on the IoT protocol CoAP.

## Slide 30
Updated as of 25 Mar 2022
[https://ih-patterns.blogspot.com/p/test.html]
Notes: [1] S. Wendzel, S. Zander, B. Fechner, C. Herdin: Pattern-based Survey and Categorization of Network Covert Channel Techniques, ACM Computing Surveys, Vol. 47, Issue 3, pp. 50:1-26, ACM, 2015. An early version of the article is available here: download. [2] W. Mazurczyk, S. Wendzel, S. Zander, A. Houmansadr, K. Szczypiorski: Information Hiding in Communication Networks, Wiley, 2016. Chapters 3 and 8 contain discussions on hiding patterns, basically on the basis of [1] but with an extension of timing-based patterns. [3] W. Mazurczyk, S. Wendzel, K. Cabaj: Towards Deriving Insights into Data Hiding Methods Using Pattern-based Approach, in Proc. Second International Workshop on Criminal Use of Information Hiding (CUING 2018) at ARES, pp. 10:1-10:10, ACM, 2018.
[4] A. Velinov, A. Mileva, S. Wendzel, W. Mazurczyk: Covert Channels in MQTT-based Internet of Things, IEEE ACCESS, Vol. 7, pp. 161899-161915, 2019.
[5] A. Mileva, A. Velinov, L. Hartmann, S. Wendzel, W. Mazurczyk: Comprehensive Analysis of MQTT 5.0 Susceptibility to Network Covert Channels, Computers & Security, Elsevier, 2021.
[6] L. Hartmann, S. Zillien, S. Wendzel: Reset- and Reconnection-based Covert Channels in CoAP. In: Proc. European Interdisciplinary Cybersecurity Conference (EICC), 2021.

## Slide 31
Evaluating Covert Channels
[Wendzel 2014]

## Slide 32
CCEAP PCAPs
Previous Practice Problems
Practice Evaluating/Categorizing

## Slide 33
Capt Daniel Fitzgerald
Questions?

## Slide 34
Covert Channel SANS White Paper [Couture 2010]
  https://www.sans.org/reading-room/whitepapers/detection/covert-channels-33413
Pattern-based Survey and Categorization of Network Covert Channels [Wendzel 2015]
  https://arxiv.org/pdf/1406.2901.pdf
  Updated here: https://ih-patterns.blogspot.com/p/test.html
Work by Wendzel
  https://www.wendzel.de/
Google
Creativecommons.org/licenses
Main References
Notes: [1] S. Wendzel, S. Zander, B. Fechner, C. Herdin: Pattern-based Survey and Categorization of Network Covert Channel Techniques, ACM Computing Surveys, Vol. 47, Issue 3, pp. 50:1-26, ACM, 2015. An early version of the article is available here: download. [2] W. Mazurczyk, S. Wendzel, S. Zander, A. Houmansadr, K. Szczypiorski: Information Hiding in Communication Networks, Wiley, 2016. Chapters 3 and 8 contain discussions on hiding patterns, basically on the basis of [1] but with an extension of timing-based patterns. [3] W. Mazurczyk, S. Wendzel, K. Cabaj: Towards Deriving Insights into Data Hiding Methods Using Pattern-based Approach, in Proc. Second International Workshop on Criminal Use of Information Hiding (CUING 2018) at ARES, pp. 10:1-10:10, ACM, 2018.
[4] A. Velinov, A. Mileva, S. Wendzel, W. Mazurczyk: Covert Channels in MQTT-based Internet of Things, IEEE ACCESS, Vol. 7, pp. 161899-161915, 2019.
[5] A. Mileva, A. Velinov, L. Hartmann, S. Wendzel, W. Mazurczyk: Comprehensive Analysis of MQTT 5.0 Susceptibility to Network Covert Channels, Computers & Security, Elsevier, 2021.
[6] L. Hartmann, S. Zillien, S. Wendzel: Reset- and Reconnection-based Covert Channels in CoAP. In: Proc. European Interdisciplinary Cybersecurity Conference (EICC), 2021.

## Slide 35
Firewalls – Packet vs Stateful vs Application
Intrusion Detection System – Automate analysis and alert
Intrusion Prevention System – Automate, alert, block
SNORT/NIDS
Moloch – Analysis tool
Endgame???
Security Onion – Blue team security OS
Signatures vs Heuristic vs Patterns
Detection
Notes: Why is detection extremely difficult? – Everything can be used for good and bad.
Only way to determine intent is after the fact.

## Slide 36
Detect vs Limit vs Eliminate
Machine Learning? (ML)
  Support Vector Machines
  Neural Networks
  C4.5 Decision Trees
Traffic Normalization (TN)
  Replace Unused/Fixed/Derivate
Statistical Approaches (SA)
Anomaly Detection Tools
  Web Tap [Borders 2004]
  Tunnel Hunter [Dusi 2008]
Detection
[Wendzel 2015]
Notes: Dr J – AI wont work, it improves efficiency, it does nothing for effectiveness. Will not improve the effectiveness of failed processes.
Traffic Normalizers – Remove ambiguities and policy breaking elements in network traffic. (i.e. replace TTL field)
- Might also set setting headers to default values
- Limited by buffer size for re-ordering or fixing timing
Statistical Approaches – Detection vs inter-arrival time pattern, random value pattern, and maybe others based on statistical value distributions
Machine Learning – Covert channels can be detected using supervised ML approaches
-SVM – can detect IP ID or TCP ISN covert channels
-NN – can detect TCP ISN
-C4.5 DT – can detect inter-packet timing channels and simple protocol switching channels
Web Tap – measures browsing patters to determine if it is a legit user
-Header format, Delay times, Request sizes, bandwidth usage (out vs in), request regularity/ time
Tunnel Hunter – statistical fingerprinting to detect network tunnels
-IP packet size, time between arrival, order of arrival
Screenshot from A Pattern-based Survey and Categorization of Network Covert Channel Techniques by Steffen Wendzel
https://arxiv.org/pdf/1406.2901.pdf

## Slide 37
Dr J video: https://drive.google.com/file/d/16HpL1qxRjlv6YxaC59_Jb3yMlKtvaJni/view?fbclid=IwAR2PlPvzaUYx6Dvmn2X0-ro398YgznFL4QzrdKxUlN7lBlHzx9LdZAWsVys
Recommend watching the entire video
7:35 for Hume’s Induction Problem
47:28 for why AI/ML wont save us (ends at 50:30)
Detection
Notes: Why is detection extremely difficult? – Everything can be used for good and bad.
Only way to determine intent is after the fact.
Dr J video: https://drive.google.com/file/d/16HpL1qxRjlv6YxaC59_Jb3yMlKtvaJni/view?fbclid=IwAR2PlPvzaUYx6Dvmn2X0-ro398YgznFL4QzrdKxUlN7lBlHzx9LdZAWsVys
7:35 for Hume’s Induction Problem
47:28 for why AI/ML wont save us (ends at 50:30)